| Reference | Description | Qty |
| --- | --- | --- |
| 10 | 17970 | STOLBERGER Машина сигарного типа 1+6, Модель SV 500 | 1 |
| 30 | 16826 | MAILLEFER 80 мм экструдер с 3 шнеками, Модель 80/20D | 1 |
| 30 | 17914 | MAILLEFER 45 мм горизонтальный дополнительный экструдер, Модель BM 45-20D | 1 |
| 30 | 17919 | NOKIA 45 мм- 24D ПВХ-ПЭ экструдер, модель NMA45-24D | 1 |
| 31 | 17915 | MAILLEFER сдвоенная экструзионная головка, Модель 115/130 | 1 |
| 31 | 17924 | 30 мм однослойная экструзионная головка | 1 |
| 31 | 17925 | Однослойная экструзионная головка, Модель 50/55 mm | 1 |
| 31 | 17935 | BETA Высокоскоростной подогрев жилы, Модель MCS280 | 1 |
| 31 | 17926 | Mapre комплект цилиндров и шнеков | 1 |
| 34 | 17916 | MAILLEFER прямая ванна охлаждения для кабелей большого диаметра. | 1 |
| 34 | 17921 | NOKIA многопроходная ванна охлаждения для автомобильных и тел. проводов | 1 |
| 41 | 17920 | NOKIA полностью автоматический сдвоенный приемник, Модель EKP 50 | 1 |
| 42 | 17896 | DRUMLESS 1500 мм Отдатчик тормозного типа | 1 |
| 42 | 17923 | Горизонтальный вращающийся отдатчик типа стол 2000 мм | 1 |
| 50 | 17929 | NORDSON Электростатический талькатор, Модель ECC500 | 1 |
| 55 | 17934 | 25 x METALUBE 205л резервуар для эмульсии для алюминия и сплавов, ALUMOL | 1 |
| 60 | 17971 | MILL 6 блочная двухярусная волочильная линия, Модель EB2 | 1 |
| 63 | 17928 | NIEHOFF Машина среднего волочения с отжигом, Модель MV250 | 1 |
| 85 | 17895 | Набор алмазных волок для волочильных машин | 1 |
| 90 | 17938 | Стальные катушки 500 X 360 X 127 (fl X O.w. X Bore In mm) | 130 |

1 X STOLBERGER Bearing Type Tubular Strander 1+6, Model SV 500 (our ref. 10– 17970)

Complete high speed bearing type tube, perfectly suitable for stranding bare Copper, Aluminium, ACSR or steel wires. Line is complete with: * External 560 mm pay-off * Tube 1+6/560 mm, on bearings * Capstan 2 x 1000 mm, with gear box * Brondel take-up 1400 mm * DC motor and electrical panel It has been used for stranding electrical conductors and is still in very good condition.

| Number of bobbin Bobbin flange dia Barrel dia Overall width Bore diameter Bobbin holding Pintle closing Wire tension Wire guides Wire break detection Speed Capstan Lay-length range Lay-length set-up Length counter Drive Power supply Braking system Stopping time Colour Protecting covers Direction | 6 560 mm 270 mm 315 mm 127 mm Between pintles Pneumatic Band brake system External TC eyelets Available Up to 1000 RPM 2 x 1000 mm 22 to 172 mm 64 speed gear box Available DC motor 52 kW 380V / 50 Hz 3 disk brakes 12 to 15 sec RAL 6011, green Available Left to right |
| --- | --- |

1 X MAILLEFER 80 mm Extruder, with 3 Screws, Model 80/20D (our ref. 30– 16826)

Reputed Maillefer extruder 80 mm 20 D well adapted for PVC/PE extrusion. Unit includes : * Main extruder with 2 speed gear box * DC motor * 3 screws Electrical panel is not included as was part of the line.

| Screw dia. Screw length Screw type Material Drive Number of zones Cooling of breach | 80 mm 20 D 2 x barrier + 1 x single flight PVC/PE DC Motor Siemens 35 kW/440V - 2500 RPM 4 Water cooling |
| --- | --- |

1 X MAILLEFER 45 mm Horiz. Piggy Back Extruder, Model BM 45-20D (our ref. 30– 17914)

This horizontal extruder is designed very compact and can swivel at the back. It is very convenient to be used as piggy back. This is an ideal solution for stripping or skinning operations. The machine is in good condition. It was working as piggy back extruder together with a 100 mm main extruder. Machine can be fixed on the floor.

| Screw dia L/D Screw speed Heating zones Motor Electrical panel X-head | 45 mm 20 12-120 rpm 4 15 kW, DC Not available Not available. |
| --- | --- |

1 X NOKIA 45 mm- 24D PVC-Pe Extruder Model NMA45-24D (our ref. 30– 17919)

Nokia extruder with screw diameter 45 mm and L/D ratio 24 for processing of PVC or PE compound. Ideal to be used as piggy back extruder Machine is mechanically complete with : - Motor - Reducer - Cylinder with heating/cooling system - Hopper loader - 2 X Plasticolor 1000 - DC motor

| Screw dia. Screw length Number of heating zone Drive | 45 mm 24 D 4 29,3 kW |
| --- | --- |

1 X MAILLEFER Dual Layer X-head, Model 115/130 (our ref. 31– 17915)

This crosshead is designed for dual layer extrusion and adapted to large cable sizes. Head is model 115/130 and can accept cables of maximum 115 mm at entry of the head. Size after insulation/sheathing is maxmum 130 mm. Head can be either used with tube tooling or compression tooling. It is available with vacuum pump. It has been used in 100+45 mm line but could be used as well with extruder up to 150 mm screw dia. Head has been used in 60 + 30 mm line. Connectng flanges can naturally be adapted to other extruder diameter.

| Model Design Max. dia. of the cable Max. dia. over insul./sheath Used with Can be used with Vaccum pump | 115/130 Dual layer 115 mm 130 mm 100+45 mm extruders up to 150 mm extruder Available |
| --- | --- |

1 X  30 mm Tube Extrusion head, Single Layer (our ref. 31– 17924)

Complete stand alone extrusion head designed to produce plastic tubes. head is fitted with: - 3 heating zones - T° sensor - P sensor (Dynisco PT450E) - Flange - Extrusion tooling (tips and dies)

| Head type Flange diameter Heating zones Tooling | Straight 128 mm 3 Up to 30 mm |
| --- | --- |

1 X Single Layer Extrusion Head, Model 50/55 mm  (our ref. 31– 17925)

Complete stand alone single layer extrusion head for general purpose applications in big insulation or medium range sheathing line. Head is delivered with: - 245 mm diameter Flange - Heating zones - 1 set of extrusion tooling inside

| Head type Diameter in Diameter out Centering | Single Layer 50 mm 55 mm Manual (4 screws) |
| --- | --- |

1 X BETA High Speed Preheater, Model MCS280 (our ref. 31– 17935)

Beta induction preheater, Model MCS 280, 34 A.

| Range of product diam. Max. section solid wire Max. section stranded wire Speed for 160 °C : 0,5-0,75 mm 0,75-1,5 mm 1,5-2,8 mm Power | 0.45 - 2.8 mm 2.8 mm² 6 mm² 2140 m/min 1050 m/min 610 m/min 16 kW |
| --- | --- |

1 X Mapre set of cylinders and screws (our ref. 31– 17926)

Set of

1 X MAILLEFER Straight Cooling Trough, for Large Cable Dia. (our ref. 34– 17916)

+/- 8m stainless steel cooling trough suitable for large cables.

1 X NOKIA Multipass Cooling Trough for AutomotiveTel Wire (our ref. 34– 17921)

Cooling ideal to be fitted in automotive or tepelphone insulation line. Line direction is Left to Right It composed with: - 4 m water section with telescopic section - 15 m straight cooling section - 80 m multipass cooling section

1 X NOKIA  Fully Automatic Double Spooler, Model EKP 50 (our ref. 41– 17920)

Ideally suited to work in line with telephone line or data cable, this machine can also be inserted in other high speed extrusion lines. The machine includes magasine for empty bobbin as well as ejector for full bobbins. Transfer as well as handling of bobbins is full automatic which allows the good running of this eqipment without operator intervention.

| Flange dia. Overall width Speed Drive Year | 500 mm 375 mm 2000 m/min 2 x DC motors about 8,3 kW 1996 |
| --- | --- |

1 X DRUMLESS 1500 mm Brake Type Pay-Off, with Expansible Shaft (our ref. 42– 17896)

This pay-off is designed with expansible shaft, pneumatically actuated, for unwinding drumless coils up to 1500 mm diameter. It is typically used before rod breakdown drawing line for paying-off off rods. It was used for 9.5 mm Aluminium rods before. It is equipped with pneumatic braking system for back tensioning the rods Pay-off is strong and horizontal type.

| Coil diameter Inner dia. Width Holding Shaft type Loading Back tensioning Direction | 1500 mm 400 to 560 mm 750 mm On shaft Expansible From side Pneumatic brake L to R or R to L |
| --- | --- |

1 X   Horizontal Rotating Table Pay Off 2000 mm (our ref. 42– 17923)

Horizontal (vertical shaft) rotating table type Pay Off for non ferrous and ferrous wires in feeding or rewinding process at low speed. Drive is included in machine frame. Suitable for copper rod coils up to 2 m diameter.

| Table dia. Type Motor Parking brake | 2000 mm Vertical 7,5 kW AC Pneumatic |
| --- | --- |

1 X NORDSON Electrostatic Powder Applicator, Model ECC500 (our ref. 50– 17929)

Very good electrostatic powder application used in cable extrusion line. Fitted with height adjustable powdering chamber which is equipped with 2 Versa Spray guns. The air dryness is ensured by a Domnick Hunter’s Pneudry DM012 Machine is mobile on castors wheels and operator panel is separated. The powdering chamber is offset from main body in order to reduce space around the cable

| Model Capacity Max flow Power Pneumatic supply Air consumption Cable passage Powdering chamber offset Powdering chamber height | ECC 500-2 500g/min 180 m³/h 0,9 kW 6 bars 30 m³/h 75 mm 550 mm ahead of main chassis Adjustable: Std height 1000 mm |
| --- | --- |

1 X 25 x METALUBE 205L lubricant for Al & Alloy draw., ALUMOL   (our ref. 55– 17934)

METALUBE, good lubricant for Aluminium and Al Alloy drawing operation. Available in barrel 205 liter, ALUMOL 195 & ALUMOL 15 - 15 ALUMOL 195, Batch 3487 - 9 ALUMOL 195, Batch 3634 - 1 ALUMOL 15, Batch 3635

| Net weight AL 195 - Batch 3487 Net weight AL 195 - Batch 3634 Net weight AL 15 - Batch 3635 | 183 kg 185 kg 176 kg |
| --- | --- |

1 X MILL 6 Block Double Deck Drawing Line, Model EB2 (our ref. 60– 17971)

Drawing line used for drawing low carbon steel rod from 6,5 mm down to 2,3 mm. Machine is composed of: * 6 drawing blocks * Control panel * Coiler * Electrical panel. Each block is driven by DC motor.

| Number of blocks Block dia Product inlet Outlet Drive block Control panel: Protection guards Electrical cabinet: Coiler Drive coiler | 6 550 mm 5,5 - 6,5 mm 2,3 to 3,5 mm DC motor 37 kW Available Available Available Available DC Motor 33kW |
| --- | --- |

1 X NIEHOFF Intermediate Drawing/Annealing unit, Model MV250 (our ref. 63– 17928)

Single wire drawing machine nicely designed with concentric shafts allowing all capstans the same sizes. All the capstans bearings have been replaced in 2010. Available with a VG30 annealer Control panel and motor not available

| N°dies Inlet Dia. Die elongation Speed Fin. Dia. Capstan Dia. Annealer Power Voltage Current Drive Electrical Panel | 17 3,0 mm 250 N/mm² 2,5 mm 400N/mm² 26% 35,5 - 50 m/s max through 2-speed gearbox 1,2- 0,32 mm 250 mm 45 kVA 35...59V 1300A not available not available |
| --- | --- |

1 X Set of Diamond Dies for Drawing Line (our ref. 85– 17895)

About 700 diamond dies used for Aluminium drawing. Mainly made by Compax and Syndie

| Inner dia Outer dia Thickness | 0.7 up to 2.4 mm 22, 25 and 28 mm 9.5, 10 and 12 mm |
| --- | --- |

130 X  Steel Bobbin 500 X 360 X 127 (fl X O.w. X Bore In mm) (our ref. 90– 17938)

| Flange diameter Barrel diameter Bore diameter OAW Useful width | 500 mm 280 mm 127 mm 360 mm 310 mm |
| --- | --- |